## Slide 1
Material Handling
And
Storage
Notes: Thank you for including me…
My background – over 25 years of commercial Property and Casualty insurance experience, specializing in marketing, product development, and the utilization of client-facing technologies.
Began career with Willis, then was with Sedgwick which became Marsh, then spent the last 15 years with WGA and came into Gallagher as a merger partner in 2015.
Beyond all my marketing years, I was a producer while at Marsh and when I started at WGA, making me uniquely qualified to know what it takes for all of you to get the kind of opportunities I want to work on with you.

## Slide 2: Material Handling and Storage

## Slide 3: Hazards
600,000 overexertion injuries, 27% of all
lost- workday cases
  370,000 injuries caused by lifting
  93,000 pushing/pulling
  Strains and sprains from loads that are too heavy or large
  Fractures, cuts, and bruises from improper storage

## Slide 4: General Work Practices
Get help for large loads
When blocking a raised load:
  Keep hands from underneath before releasing load
  Use blocking materials of adequate strength
  Look for cracks, splintered pieces, rounded corners, etc.
Attach handles or holder to loads
PPE
  Gloves, eye protection, safety boots (for heavy loads)

## Slide 5: Mechanical Material Handling
Do not overload equipment
Refer to equipment rated capacity
General forklift procedures
  Center load on forks and close to mast
  Do not overload
  Do not add extra weight to counterbalance
  Travel with load at lowest position

## Slide 6: Materials Storage
Stacked loads correctly piled and cross-tiered
Stored material must not create hazard
Areas free of accumulated material
In buildings, no stored materials within 6 feet of hoist ways or 10 feet of exterior building walls
Store non-compatible material separately

## Slide 7: Lumber and Brick Storage
Lumber
  Maximum stack height
    16 feet (manual handling)
    20 feet (forklift)
  Remove nails from used lumber
  Stacks stable and self-supporting
Bricks
  Maximum 7 feet high
  Above 4 feet, taper stacks 2 inches per foot

## Slide 8: Block and Bag Storage
Masonry blocks
  Above 6 feet , taper stacks 2 blocks per tier
Bags and bundles
  Stack in interlocking rows
  Step back at least every 10 layers
  Remove from top of stack first
  Keep baled paper and rags at least 10 inches from walls, ceilings, or sprinkler heads

## Slide 9: Box and Drum Storage
Boxed materials
  Hold in place using cross-ties or shrink plastic
Drums, barrels, kegs
  Stacked symmetrically
  If stored on side, block bottom tiers to prevent rolling
  If stacked on ends, use planks, pallets, etc. between each tier
Block cylindrical material (bars, poles, etc.)
Use bins or shelves for materials that cannot be stacked

## Slide 10: Manual Lifting
Avoid manual lifting when possible
Limit vertical lifting (knuckle-to-shoulder height)
Be in good physical shape
Plan the lifting operation
Get a good grip
Keep the load close to the body
Do not twist or bend sideways
Get help for large or heavy loads

## Slide 11: Manual Lifting
Recommendations for specific tasks
  Grasp opposite corners on boxes, cartons & sacks
  Use mechanical assistance for barrels and drums
  Wear leather gloves when handling sheet metal
  Plate glass
    Carry with bottom edge in gloved palm, other hand on top edge
    Never carry plate glass under the arm
  Use a team for long objects

## Slide 12: 2-wheeled hand trucks
Tip load forward and slip tongue underneath
Keep center of gravity low
Let the truck carry the load - don't lean it too far
Walk forward - keep load height low enough to see
Secure bulky items to the truck
Use specialty equipment
  Drums
  Appliances